## Slide 1
Notes: Click Tools->Library Repository

## Slide 2
Notes: In the Library Repository window click "Install..."

## Slide 3
Notes: In the Select Library window browse to and select the PMC .compiled-library file. Then click "Open"

## Slide 4
Notes: Open the Library Manger from the Devices tree. Then click "Add library"

## Slide 5
Notes: Search for and find the PMC library and click "OK"

## Slide 6
Notes: The task that calls the PMC function blocks should be the same task responsible for the Ethercat Bus Cycle. You can either move the PLC_PRG to the EtherCAT_Task or give the MainTask the Bus Cycle. This example chooses the later. Double click the EtherCAT Master. Then go the EtherCAT I/O Mapping tab and switch the Bus cycle task to the MainTask

## Slide 7
Notes: Then make sure that the MainTask’s cyclic interval (double click MainTask) and the EtherCAT Master’s cycle time (General tab in the EtherCAT Master) are at the same time.

## Slide 8
Notes: In the PLC_PRG POU declare a PMCLib.PMControllerType variable

## Slide 9
Notes: Double click the PMC device (Communication Protocol A) and go to the EtherCAT I/O Mapping tab. Switch the Always update variables option to Enable 2 (always in bus cycle task)

## Slide 10
Notes: Map the DataToPMCArray channel to the DataToPMC member of the PMControllerType variable you declared in the PLC_PRG. Map the DataFromPMCArray channel to the DataFromPMC member of the PMControllerType variable

## Slide 11
Notes: Before using the PMC library, make sure that one and only one instance of the PMC_AutoRefresh function block is declared and that the PMC_AutoRefresh function block is called once and only once per PLC cycle